## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
CNOEC PROJECT
Gabriele Ribolla Enrico Tranquillini
Matteo Constantini

## Slide 2: Team
Enrico Tranquillini
B.S.: Automation Engineering (Polimi)
M.Sc: Automation and Control Engineering (Polimi)
Matteo Costantini
B.S: Automation Engineering (Unibo)
M.Sc: Automation and Control Engineering (Polimi)
Gabriele Ribolla
B.S.: Industrial Automation (UniBS)
M.Sc: Automation and Control engineering (PoliMi)

## Slide 3: Project : qualitative goal
Goal: route optimization along a track using a drone.

## Slide 4: Project : reason why we chose the specific topic
Passions and interests about autonomous vechicles and Flight

## Slide 5: Procedure to define the lap time
Steps
1:
define the optimal trajectory
using :
optimal trajectory function
2:
compute the speed profile and lap time
using :
speed profile function aware of constraints
3:
use nonlinear quadmotor model to compute final control inputs

## Slide 6: 1° step : Main cost function and Contraints

## Slide 7: Project : the main cost functions and contraints
Optimal trajectory and lap time
Cost function: J
;
= ;
parameters tuning in the cost function
Constraints: racing line in the track boundaries and acceleration (not vehicle ones)

## Slide 8: Cost Function

## Slide 9: Quadcopter model

## Slide 10: Flight physics

## Slide 11: Kinematics of the system

## Slide 12: Dynamics of the system

## Slide 13: Aerodynamics of the propellers and definition of the inputs

## Slide 14: Non linear mathematical model

## Slide 15: Modelization
function [zdot]=quadcopter(t,z,u,th)
%% Read parameters, states and inputs
% Parameters
mass = th(1,1);
Jx = th(2,1);
Jy = th(3,1);
Jz = th(4,1);
g = th(5,1);
% States
X = z(1,1); % inertial X position (m)
Y = z(2,1); % inertial Y position (m)
Z = z(3,1); % inertial Z position (m)
xbdot = z(4,1); % body x velocity (m/s)
ybdot = z(5,1); % body y velocity (m/s)
zbdot = z(6,1); % body z velocity (m/s)

## Slide 16: Modelization
psi = z(7,1); % yaw angle (rad)
theta = z(8,1); % pitch angle (rad)
phi = z(9,1); % roll angle (rad)
p = z(10,1); % inertial p rate (rad/s)
q = z(11,1); % inertial q rate (rad/s)
r = z(12,1); % inertial r rate (rad/s)
% Inputs
T = u(1,1); % thrust force (N)
tauroll = u(2,1); % roll torque (N*m)
taupitch = u(3,1); % pitch torque (N*m)
tauyaw = u(4,1); % yaw torque (N*m)
%semplifications
cp=cos(psi);
sp=sin(psi);
ct=cos(theta);
st=sin(theta);
cf=cos(phi);
sf=sin(phi);

## Slide 17: Modelization
%% Model equations
zdot(1,1) = cp*ct*xbdot+(cp*st*sf-sp*cf)*ybdot+(sp*sf+cp*cf*st)*zbdot;
zdot(2,1) = ct*sp*xbdot+(cf*cp+sp*st*sf)*ybdot+(cf*st*sp-cp*sf)*zbdot;
zdot(3,1) = -st*xbdot+ct*sf*ybdot+ct*cf*zbdot;
zdot(4,1) = r*ybdot-q*zbdot+g*st;
zdot(5,1) = -r*xbdot+p*zbdot-g*ct*sf;
zdot(6,1) = q*xbdot-p*ybdot-g*ct*cf+T/mass;
zdot(7,1) = -(sf/ct)*q+r;
zdot(8,1) = cf*q+sf*r;
zdot(9,1) = p+(sf*st/ct)*q-(cf*st/ct)*r;
zdot(10,1) = (tauroll/Jx)-((Jz-Jy)/Jx)*r*q;
zdot(11,1) = (taupitch/Jy)-((Jx-Jz)/Jy)*r*p;
zdot(12,1) = (tauyaw/Jz)-((Jy-Jx)/Jz)*p*q;

## Slide 18: Simulation
%% Model parameters
Jx=0.0058319;
Jy=0.0058319;
Jz=0.0111886;
I_drone = [ ...
Jx, 0, 0;
0, Jy, 0;
0, 0, Jz;
] ; % (kg.m^2)
mass = 0.9272;%(kg)
g=9.81;
Tmax=45;%(N)
taurollmax=0;%(Nm)
taupitchmax=0.58;
tauyawmin=-0.58;
th = [mass;Jx;Jy;Jz;g];

## Slide 19: Simulation
%% Simulation: Initial state
Vb_init = [0;0;0]; % (m/sec) initial velocity in BODY axes
wb_init = [0;0;0]; % (rad/sec) initial body rates
eul_init = [0;0;0]; % (rad) initial euler angles (yaw,pitch,roll)
Xe_init = [0;0;0]; % (m) initial position in inertial axes
%state vector INITIAL conditions
q_init = [ Xe_init;
Vb_init;
eul_init;
wb_init];
%% Simulation with ode45
% Time integration parameters
Ts_o45 = 1e-1; % sampling time (s)
Tend_o45 = 200; % final time (s)
tvec_o45 = 0:Ts_o45:Tend_o45; % time vector (s)

## Slide 20: Simulation
% Initialize simulation output
N_o45 = length(tvec_o45); % number of samples
zout_o45 = zeros(12,N_o45); % matrix with states
uout_o45 = zeros(4,N_o45); % matrix with inputs
zout_o45(:,1) = q_init;
uout_o45(:,1) = [1+mass*g;1;1;1];
% Run simulation
for ind=2:N_o45
zout_temp = ode45(@(t,z)quadcopter(t,z,uout_o45(:,ind-1),th),[0 Ts_o45],zout_o45(:,ind-1));
zout_o45(:,ind) = zout_temp.y(:,end);
uout_o45(:,ind) = uout_o45(:,1);
end

## Slide 21: Results

## Slide 22: Results

## Slide 23: Results

## Slide 24: Results

## Slide 25: Simulation of the nonlinear model (Simulink)
The simulation of the uncontrolled non linear model takes as inputs some references of altitude,roll,pitch,yaw commands and plots the states of the system

## Slide 26: Project : Plan
Complete:
3/12/2021: unconstrained optimization model
22/12/2021: integration with quadcopter model

## Slide 27
Questions??

## Slide 28
Thanks for the attention